## Slide 1: Hot Pixels: Frequency, Power, and Temperature Attacks on GPUs and Arm SoCs
Hritvik Taneja, Jason Kim, Jie Jeff Xu Stephan van Schaik, Daniel Genkin, Yuval Yarom
Notes: Hello, everyone. My name is Hritvik Taneja, and I will talk about our paper, Hot Pixels: Frequency, Power, and Temperature Attacks on GPUs and Arm SoCs.

## Slide 2: Evolution of Side-Channel Attacks
Microarchitectural Side-Channels
Equipment: Software
Advantages: No physical proximity, can attack remotely
Hybrid Side-Channels
Equipment: Software
Advantages: Can attack remotely, difficult to mitigate, usually works across different microarchitectures
In this work, we show
Hybrid side-channels are everywhere
Exploit them from unprivileged native user
And, even from browser!
Physical Side-Channels
Equipment: Oscilloscope, EM Probes etc.
Advantages: Difficult to mitigate, usually works across different microarchitectures
Notes: Leaked information about physical properties, such as power consumption and EM radiations.
These early attacks required specialized equipment like Oscilloscopes and EM Probes.
Difficult to mitigate since they exploit inherent physical properties.
which is also the reason that they are usually independent of microarchitecture and hence work across different microarchitectures.
As technology progressed, we witnessed the emergence of software-visible microarchitectural side-channel attacks. They didn't require any external equipment, because side channel leakage is now software visible. This means that we can mount these attacks remotely There is a third class of attacks called hybrid side channels where we get best of both worlds. These side channels exploit the physical properties such as power and temperature But instead of relying on specialized hardware, this channel relies of software API from internal sensors to measure this information. In our work, we show that They are present everywhere, desktops, laptops, mobile phones and even on GPUs. we study these hybrid side channels in the ARM SoCs, as well as GPUs.

## Slide 3: A sneak peek of our work
Frequency
Power
Temperature
Notes: Here’s a sneak peek of our work. We show that different devices try to balance a three-way tradeoff between frequency, power, and temperature. 3 dogs eating for the same bowl is a pictorial representation of this 3-way tradeoff.

## Slide 4: A sneak peek of our work
Frequency
Power
Temperature
Pixel Stealing
History Sniffing
Website Fingerprinting
Original
Leaked
When one property becomes an operational constraint, other two leak
Notes: And in order to balance these 3 properties, we see leakge from two of them when one becomes an operational constraint. Power Limit in the CPUs Finally, we use the data leakage from the hybrid side channel to mount a pixel stealing, history sniffing and website fingerprinting attack on chrome and safari. We leak this chrome logo across security domains from chrome. Okay now where do we actually start for all of this? Before talking about attacks and side channels I need to talk about machine cooling.

## Slide 5: Machine Cooling
Typical cooling configuration
Mac motherboard
The more transistors we put on a chip the hotter it runs
We need big heat sinks to keep the CPU cool and running
Which makes laptops big and bulky, we don’t like that!
Dynamic Voltage and Frequency Scaling (DVFS)
  Power or Thermal Limits
  Run fast till it gets too hot
  Slow and cool down. Repeat
Does this idea have any security consequences?
Notes: Typically, the cooling configuration on desktop CPUs involves a large heat sink, as shown in the image. However, this kind of huge heat sink cannot fit into laptops due to space constraints. Laptops often have smaller heat sinks which lack sufficient heat dissipation capacity for a CPU running at maximum utilization. To prevent the CPU from overheating and potentially burning itself to the ground, laptop CPUs adhere to certain thermal or power limits. They implement DVFS to reduce the frequency and adhere to these limits when the CPU is at risk of hitting these thermal or power limits.
Now, we have this wonderful idea, does this have any security consequences? The fact that I dedicated an entire slide for it and am standing here means that there are security consequences. In order to understand these, we perform these two experiments.

## Slide 6: Is DVFS data-dependent?
uint64_t val = 0; while (1) { val = val + 1;
}
uint64_t val = 0; while (1) { val = val + 0;
}
M1 MacBook Air
M1 MacBook Pro
Notes: To answer that question we run these two workloads, the first workload repeatedly increments a variable by 1 and the second workload increments a variable by 0. M1 MacBook Air:
- Temperature Same - Frequency and Power is different
The next device on which we run these workloads is an M1 MacBook Pro. We can see that the plots for it look different from the M1 MacBook Air despite having the same chip. Well the plots are not the only different thing between two devices, there is also a price difference of 300 dollars. Where did these 300 dollars go, apple used it to buy a fan. The M1 Macbook Pro is actively cooled.
M1 MacBook Pro:
- Actively Cooled enough to dissipate heat produced by the M1 at maximum utilization
- Temperature Same - Frequency and Power is different Because the M1 Macbook Air struggles to maintain temperature, we classify

## Slide 7: Is DVFS data-dependent?
M1 MacBook Air
M1 MacBook Pro
Thermally Constrained
Frequency Constrained
Notes: M1 MacBook Air:
struggles to maintain temperature while leaking from Frequency and Power
we classify it as thermally constrained.
M1 MacBook Pro:
Same frequency but leakage from Temperature and Power
we classify it as Frequency constrained.
Next Slide:
CPUs are not the only device that compute on secret data

## Slide 8: What about GPUs?
GPUs have 1000s of cores
They run hot
They have massive cooling fans
But is it enough to cool it?
  No 
GPUs also implement DVFS 
M1 MacBook Air
AMD Radeon RX 6600
Notes: 1000s of cores.
They run hot They have massive colling fans and lots of memes
Next Slide:
Now that we have different rendering time for black pixels and white pixels, what do we do with this?
Pixel Stealing attacks.

## Slide 9: Pixel stealing attack in Chrome – Primer
SVG Filters can turn this …
Notes: Before talking about Pixel Stealing Attacks,
We first need to understand SVG filters.

## Slide 10: Pixel stealing attack in Chrome – Primer
SVG Filters can turn this …
Into this, using <feGaussianBlur stdDeviation="3"/>
Various effects:
  <feGaussianBlur> → blur
  <feColorMatrix> → color saturation

## Slide 11: Pixel stealing attack in Chrome – Primer
SVG Filters can turn this …
Into this, using <feGaussianBlur stdDeviation="3"/>
Various effects:
  <feGaussianBlur> → blur
  <feColorMatrix> → color saturation
Can be applied to:
  <div>, <iframe> or any other element
Can compute on pixels across security boundaries
Stackable!
  Stack until the GPU catches fire
  Or in our case just throttles
Notes: Next Slide:
Now I am going to give a high level overview of the technique used by pixel stealing attacks to compute and infer pixels across security boundary.

## Slide 12: Pixel stealing attack in Chrome
attacker.com
<iframe src="victim.com">
Hot Pixels
<feGaussianBlur stdDeviation="1"/> <feGaussianBlur stdDeviation="2"/>
<feGaussianBlur stdDeviation="3"/>
<feColorMatrix type="matrix" values="-6.88 …. "/> <feGaussianBlur stdDeviation="4"/>
          …
SVG Filter Application
Chart: 
| April | May
Region 1 | 25 | 75
Fast = Black
Slow = White
Chart: 
| April | May
Region 1 | 50 | 50
GPU Throttling
Using CSS
Notes: - Attacker.com embeds victim.com as an iframe.
- Chrome doesn’t allow attacker.com to read the contents of the embedded iframe.
- So what do we do now?
- Isolate a single pixel and scale it to the entire screen, we use a bunch of CSS tricks to do this.
- Next we apply a bunch of filters and measure the time it takes to apply them.
- Filter application produces 2 outputs the first one is the resulting pixels which looks something like this
- And the second one is a throttling GPU
- Now, Based on the time it takes to render the pixel we either classifiy the pixel as black or white.

## Slide 13: Pixel stealing attack in Chrome - Results
Works on: Laptops, Phones with integrated GPUs and desktops with discrete GPUs.
Time to steal a pixel: 10-20 sec
Accuracy: 60-80%
Original
Notes: Here are the results of the pixel stealing attack across multiple devices. The attack works on the macbook airs, pixel 6 pro, oneplus 10 pro and nvidia and AMD discrete GPUs The next most popular browser after chrome is safari? What about safari?

## Slide 14: History sniffing attack in Safari
Safari does not serve cookies across iframes
Countermeasure to Pixel Stealing
  Can’t steal what is already public
Can we steal something?
Users’ Browsing History
attacker.com embeds links (<a>)
Isolate a pixel and perform Pixel Stealing
Works on: M1, M2 MacBook Air and iPhone 12, 13
Time to recover per link: 200-250 seconds
Accuracy: 90-100%
Welcome,
Hritvik
Welcome,
New User
Notes: What does this mean? Lets say we embed an iframe in chrome.
Chrome will serve the cookie to this embedded iframe So if I am logged in to a website and open it in an iframe, chrome will serve cookie to embdded iframe, which means chrome knows who I am and I'll see something like welcome Hritvik
Now safari doesn;'t serve cookie to an embdded iframe, which means an embdded iframe in safari has no way of knowing who I am, so we see a generic text such as welcome new user. Okay, so This is the history sniffing attack.

## Slide 15: Website Fingerprinting
google.com
amazon.com
nytimes.com
macOS provides API measure GPU frequency and power
Accessible by unprivileged user
This is a huge security problem
  Any random person can read your frequency and power
Fingerprint Websites accessed by colocated user
Accuracy / 100 Websites:
  Top 1: 27%
  Top 2: 37%
  Top 5: 49%
  Baseline: 1%
Notes: Our last attack is a website fingerpriting attack? So how do we go about it. Any random person can read your GPU frequency and power while you compute on it.
We can also read them while someone is browsing the internet. To show how this can be exploited, we mount a website fingerprinting attack. Here we see the GPU frequency and power traces when rendering three websites.

## Slide 16: Thank you for listening! Questions? htaneja3@gatech.edu
3-way tradeoff between Frequency, Power and Temperature
Data Dependent CPU and GPU throttling behavior
Attacks across multiple devices
Pixel Stealing, History Sniffing, Website Fingerprinting
Summary
Original
Leaked
Notes: Just like we can